## Slide 1: Local Networking with Distant Warmup
Often the warmup room is far
Marshall is in the warmup room
Safest solution is to connect a second router, by wire.
  WAN Port of second router goes to one of the 4 LAN ports of the main router
Note for main room:
  Owlcms is connected by wire
  Announcer and timekeeper are normally very close to router, WiFi is OK
  Athlete-facing is far from router, so LAN wiring is suggested.
  Scoreboards are far. Wiring the main one is ideal, but not mandatory.

## Slide 2
Attempt Board + Secondary Scoreboards (WiFi)
Referee devices (USB)
Owlcms (LAN!)
Marshall (WiFi*)
Announcer
(WiFi*)
Competition Network (192.168.1.x)
Athlete-facing display (LAN)
This Photo by Unknown Author is licensed under CC BY
This Photo by Unknown Author is licensed under CC BY
publicresults
Individual Scoreboards
Warmup Network (192.168.x.y)
Main Router
Warmup
Router
WAN
Main Scoreboard (LAN)
Warmup Scoreboard (LAN)
Timekeeper (WiFi)
LAN 1-4
LAN 1-4

## Slide 3: Isolated Setup for Individual Scoreboards
This setup reverses the role of the routers to prevent vandalism of the competition network
  The « main » router is the one in the warmup area and acts as the WAN
  The competition floor router is protected because the machines on the brown network cannot see the machines in the blue network
  The setup works because owlcms initiates the connection to publicresults
If you also need other machines in the attendance network that need to connect back to owlcms, then
  The blue router must open of its ports (for example, port 8080) and redirect it to owlcms
  The machines on the brown network will use the address of the blue router as seen on the brown network, and use that as their destination.

## Slide 4
Scoreboards
Referee devices (USB)
owlcms 192.168.4.100
Marshall
Announcer
Competition Network (192.168.4.x)
Athlete-facing display
This Photo by Unknown Author is licensed under CC BY
This Photo by Unknown Author is licensed under CC BY
publicresults 10.0.0.234
Individual Scoreboards
Attendance Network (10.0.0.x)
Competition Router
Crowd/Coaches
Router + WiFi
WAN

## Slide 5: Video Isolation
In this setup, the network traffic for the video streaming does not reach the competition network
This requires a port forwarding rule to be put in place on the competition router
  In the example, the OBS machine sees the competition router as 10.0.0.1
  The blue router forwards outside requests for port 8080 to 192.168.1.100:8080
  OBS therefore uses 10.0.0.1:8080 to see owlcms

## Slide 6
Scoreboards
Referee devices (USB)
owlcms 192.168.1.100
Marshall
Announcer
Competition Network (192.168.1.x)
Athlete-facing display
This Photo by Unknown Author is licensed under CC BY
This Photo by Unknown Author is licensed under CC BY
10.0.0.110
Competition Router
Video Station (OBS)
WAN
WAN
10.0.0.1

## Slide 7: Full Networking Setup
Competition Network
Owlcms connected to main router using its 192.168 address
One additional secondary router per additional platform
Additional Ethernet switches be added
Owlcms should have a fixed, reserved DHCP address to support port redirection
Video Network
Connects to internet, acts as internet gateway for main router
No video traffic goes to main router, uses a port redirection to see owlcms
Public Network
The public can follow the scoreboard with Heroku

## Slide 8: Networking Setup
The following pages show several networking configurations, in increasing order of capability
Goals:
  To use normal home networking equipment (consumer-grade routers, switches and access points) you can get at the normal electronics outlets
  To limit configuration to what a regular hobbyist normally does (set the Wi-Fi names, open gaming ports)

## Slide 9
10.0.0.234
192.168.0.1
Owlcms DHCP Reservation 192.168.0.100:8080
WAN
192.168.0.100:8080
Main Router
Wi-Fi 1 192.168.1.122
LAN 1 192.168.0.110
Competition Network
All machines see owlcms using its 192.168 address
Simplest setup
One main router
WAN can connect to internet if needed.
Even with good Wi-Fi, the main laptop is wired
Optionally, you can wire the announcer, etc.
Physical or WIFI connection
IP Connection

## Slide 10
10.0.0.234
192.168.0.1
Owlcms DHCP Reservation 192.168.0.100:8080
WAN
192.168.0.100:8080
Main Router
Switch for additional ports
Wi-Fi 1 192.168.1.122
LAN 1 192.168.0.110
Competition Network
All machines see owlcms using its 192.168 address
Wired setup (bad Wi-Fi or long distances)
One main router
WAN can connect to internet if needed.
For remote rooms
Connect a switch to the router, or
Connect an access point to the router, or
Connect a router to the router (see next page)
Additional Access Point
Physical or WIFI connection
IP Connection

## Slide 11
10.0.0.234
192.168.0.1
192.168.0.240
Wi-Fi 2 192.168.1.115
Owlcms DHCP Reservation 192.168.0.100:8080
WAN
WAN
192.168.0.100:8080 (via default gateway)
Main Router
Secondary Router
192.168.1.1
Wi-Fi 1 192.168.1.122
LAN 1 192.168.0.110
Competition Network
All machines see owlcms using its 192.168 address
One secondary router per additional platform or room
LAN 2 192.168.1.165
Distant room using routers
You can connect a router to any of the LAN ports
On the secondary router(s)
  For simplicity use different names for each Wi-Fi networks
  Ideally, change the Wi-Fi channel to be different
Physical or WIFI connection
IP Connection

## Slide 12
10.0.0.234
192.168.0.1
192.168.0.240
Wi-Fi 2 192.168.1.115
Owlcms DHCP Reservation 192.168.0.100:8080
WAN
WAN
192.168.0.100:8080 (via default gateway)
Main Router
Secondary Router
Switch for additional ports
Switch for additional ports
192.168.1.1
Wi-Fi 1 192.168.1.122
LAN 1 192.168.0.110
Competition Network
All machines see owlcms using its 192.168 address
One secondary router per additional platform or room
LAN 2 192.168.1.165
Multiple platforms
To minimize configuration and keep things simple,
  Connect the other platform routers directly to the main router
  Use different Wi-Fi names
  Use different channels
You can connect one or more switches or access points to each router if you need more ports.
Additional Access Point
Physical or WIFI connection
IP Connection

## Slide 13
107.171.217.85
10.0.0.234
10.0.0.1
192.168.0.1
192.168.0.240
Wi-Fi 2 192.168.1.115
Internet Router
Owlcms DHCP Reservation 192.168.0.100:8080
OBS
WAN
WAN
WAN
10.0.0.234:8080 port redirection configured on router 1 for 192.168.0.100:8080
192.168.0.100:8080 (via default gateway)
Main Router
Secondary Router
Switch for additional ports
Switch for additional ports
192.168.1.1
Wi-Fi 1 192.168.1.122
LAN 1 192.168.0.110
Heroku publicresults
YouTube Facebook streaming
Competition Network
All machines see owlcms using its 192.168 address
One secondary router per additional platform
LAN 2 192.168.1.165
Additional Access Point
Physical or WIFI connection
Isolated Video Network
Needs a redirection to see owlcms
Avoids video traffic hitting the competition router
IP Connection