## Slide 1: Local Networking with Distant Warmup
Often the warmup room is far
Marshall is in the warmup room
Safest solution is to connect a second router, by wire.
  WAN Port of second router goes to one of the 4 LAN ports of the main router
Note for main room:
  Owlcms is connected by wire
  Announcer and timekeeper are normally very close to router, WiFi is OK
  Athlete-facing is far from router, so LAN wiring is suggested.
  Scoreboards are far. Wiring the main one is ideal, but not mandatory.

## Slide 2
Attempt Board + Secondary Scoreboards (WiFi)
Referee devices (USB)
Owlcms (LAN!)
Marshall (WiFi*)
Announcer
(WiFi*)
Competition Network (192.168.1.x)
Athlete-facing display (LAN)
This Photo by Unknown Author is licensed under CC BY
This Photo by Unknown Author is licensed under CC BY
publicresults
Individual Scoreboards
Warmup Network (192.168.x.y)
Main Router
Warmup
Router
WAN
Main Scoreboard (LAN)
Warmup Scoreboard (LAN)
Timekeeper (WiFi)
LAN 1-4
LAN 1-4

## Slide 3: Isolated Setup for Individual Scoreboards
This setup reverses the role of the routers to prevent vandalism of the competition network
  The « main » router is the one in the warmup area
  The competition floor router is protected because the machines on the brown network cannot see the machines in the blue network
  The setup works because owlcms initiates the connection to publicresults
If you also need other machines in the attendance network that need to connect back to owlcms, then
  The blue router must open of its ports (for example, port 8080) and redirect it to owlcms
  The machines on the brown network will use the address of the blue router as seen on the brown network, and use that as their destination.

## Slide 4
Scoreboards
Referee devices (USB)
owlcms 192.168.4.100
Marshall
Announcer
Competition Network (192.168.4.x)
Athlete-facing display
This Photo by Unknown Author is licensed under CC BY
This Photo by Unknown Author is licensed under CC BY
publicresults 10.0.0.234
Individual Scoreboards
Attendance Network (10.0.0.x)
Competition Router
Crowd/Coaches
Router + WiFi
WAN