## Slide 1: owlcms: Large Venue Setup
Goals:
  Robustness:
    Continuity in case an internet outage
    Continuity if some equipment fails
  Absence of performance impacts from Video Streaming
  Ability to scale up to multiple platforms if required
  Minimize cabling (less ethernet cabling, less electrical cabling)
Design Principles
  Competition software runs locally
  All competition computers are connected to competition-only switches
  Competition traffic does not go through the router (remains within the switches)
  Router is used to shield access from the outside, to send the video and results to the internet, and to provide IP addresses to the machines on the network.

## Slide 2: Networking Setup
Owlcms
OBS
107.171.217.85
192.168.0.1
WAN
Competition Router
Heroku publicresults
Video streaming
WiFi Access Point
Physical or WIFI connection
IP traffic
WiFi Access Point
Additional switch for platform 2
X
PoE-capable Switch (one per platform)
PoE
PoE
scoreboard
Switches
Main laptop is wired to the first platform switch
Redundant WiFi Access Points powered over Ethernet (PoE).
Announcer, referee, attempt board can be wired if desired using free ports
No interference from video traffic
One platform = one switch, other switches connect directly to main switch
Router
Provides DHCP addresses
Allows OBS to fetch scoreboards from owlcms
Allows OBS to stream out
Allows owlcms to feed Heroku public scoreboards

## Slide 3: Recommendations for equipment
Use a video-capable (gaming) router
Small-business Power-over-Ethernet (PoE) switches
  For example tp-link TL-SG1008P has 4 PoE ports, 4 normal ports, handles 1Gbps.
  Use one per platform
  PoE switches allow connecting WiFi access points without having to bring electrical wiring
Redundant WiFi access points
  For example, tp-link AC1200 EAP225 Outdoor
    can be mounted on a phone tripod, correct wave shape
    disk-shaped antennas are meant for upside-down ceiling mount
  Use one (or more) access point for the main platform area, one for warm-up area
  Use the vendor’s management software to create a single unified WiFi network with redundancy and roaming (e.g. tp-link Omada)
  Use proper length Ethernet cables, avoid needlessly long cables, check connectors

## Slide 4: Considerations for Sound
Connect the sound input for down and timer sounds to the athlete-facing display.
  Sounds are emitted immediately on decisions, directly from the browser
  This avoids multiple hops through the server and back through another browser
Use a dedicated speaker for the timer and down signal
  A speaker with a « line in » and a built-in amplifier works well
    Alternately, any good quality wired PC speaker can do – but do not use Bluetooth/Digital speakers because of perceptible lag
  Going through the announcer public-address mixer is often problematic
    If the sound output is through a laptop headphone jack, it can be very difficult to set a sound mixer to work well with both announcer voice and the sounds

## Slide 5: Miscellaneous
Use a well-ventilated laptop as the main owlcms computer. Wire the main computer using ethernet wiring.
Use a separate laptop for the competition clerks
  This is the only laptop that needs Office (or compatible) and a printer
  All other laptops can use a Linux distribution with Chromium to avoid having to perform updates before every meet.
All PCs used should be known to run cool even after a day.
Get a walkie-talkie app for communications between marshall and announcer